## Slide 1: Image Transformations
Concept, Requirement, Types , Tools, Applications
Computer Vision, 6th Semester, 2024

## Slide 2: Image Transforms
An image transform can be applied to an image to convert it from one domain to another.
Viewing an image in domains such as frequency or Hough space enables the identification of features that may not be as easily detected in the spatial domain.
Other applications:
  Compression
  Filtering
  Warping/morphing

## Slide 3: Types and Applications
Spatial-to-Frequency transforms:
  Hough Transform
    used to find lines in an image
  Discrete Cosine Transform
    used in image and video compression
  Discrete Fourier Transform
    used in filtering and frequency analysis
  Haar Wavelet Transform
    used to perform discrete wavelet analysis, denoise, and fuse images
  Karheunen—Loeve Transform
  Walsh Transform
  Hadamaard Transform
  Radon Transform, etc.
Other transforms:
  Distance Transform
  Parametric Transform
  Mesh-based Warping

## Slide 4: Features highlighted
Distance Transform:
  the thickness of image features
Fourier Transform:
  the spatial frequency composition of the image
Hough Transform
  the parameters of geometric shapes.

## Slide 5: Distance Transform
Using distance metrics to depict binary image as distance coefficients
Each foreground pixel (1) is shown as the nearest distance from neighbouring background pixels (0).
Distance metrics are used:
  Euclidean distance: square root of sum of squares of x and y differences
  Manhattan/City-block distance: sum of absolutes of x and y differences
  Chessboard distances: maximum of absolutes of x and y distances
  Other:
    Chebyshev Distance
    Cosine Similarity
    Hamming Distance
    Minkowski Distance
    Mahalanobis Distance
    Earth Mover's Distance (Wasserstein Distance)

## Slide 6: Distance Transform

## Slide 7: Distance Transform – Merits and Demerits
Merits
Shape Analysis
Skeletonization
Image Segmentation
Medial Axis Extraction
Simplicity in:
  Object Recognition
  Image Registration
Demerits
Computationally Intensive
Sensitivity to Noise
Discretization Effects
Limited to Binary Images
Directionality
Parameter Sensitivity
Boundary Artifacts

## Slide 8: Discrete Fourier Transform
Used to analyze the frequency content of images
Transforms an image from its spatial domain (pixel values) to its frequency domain
Reveals information about the variation in intensity and spatial frequencies present in the image

## Slide 9: Discrete Fourier Transform
Formula
Basis Images
Example

## Slide 10: 2d D.f.t. – Utility
Frequency Analysis
Image Filtering
Compression
Feature Extraction
Image Reconstruction
Noise Removal
Pattern Recognition
Fourier Descriptors

## Slide 11: 2D D.F.T. – Merits and Demerits
Merits
Frequency Analysis
Image Filtering
Shift Invariance
Convolution Theorem
Image Reconstruction
Orthogonality
Phase Information
Demerits
Computational Complexity
Boundary Effects
Loss of Spatial Information
Sensitivity to Noise
Memory Requirements
Limited Directional Information

## Slide 12: Discrete Cosine Transform
Similar to DFT
Advantageous in terms of:
  Energy compaction
  Ability to represent image data in a more compact form
Well-suited for applications of compact representation and efficient coding
  Digital image and video compression standards

## Slide 13: Discrete Cosine Transform
Formula
Basis Images

## Slide 14: Discrete Cosine Transform
Energy Compaction Property
Reconstruction (Usage in J.P.E.G. Compression)
Inverse DCT(100%)
Inverse DCT(75%)
Inverse DCT(50%)
Inverse DCT(25%)

## Slide 15: 2D D.C.T. – Utility
Image Compression (JPEG Compression)
Energy Compaction
Image Reconstruction
Feature Extraction
Image and Video Coding
Watermarking and Steganography
Reduction of Blocking Artifacts
Signal Processing Applications

## Slide 16: 2D D.C.T. – Merits and Demerits
Merits
Energy Compaction
Compression Efficiency
Real-Valued Coefficients
Reduction of Blocking Artifacts
Computational Efficiency
Image Reconstruction
Application in Video Compression
Low Sensitivity to Small Perturbations
Demerits
Limited Spatial Information
Lossy Compression
Boundary Effects
Sensitivity to Block Size
Limited Directional Information

## Slide 17: Hough Transform
Used in image processing and computer vision for the detection of shapes, particularly straight lines and circles, in an image
Primary purpose:
  Identify instances of simple geometric shapes within an image, even when they are partially obscured, distorted, or incomplete
Most common forms:
  Hough Line Transform
  Hough Circle Transform

## Slide 18: Hough Line Transform
The Hough Line Transform is used for detecting straight lines in an image.
In its basic form, each point (x, y) in the image space corresponds to a sinusoidal curve in the parameter space (Hough space).
The intersection of curves in the Hough space indicates the parameters (slope and intercept) of a line in the image space.
By setting a threshold in the Hough space, one can identify the parameters corresponding to the lines in the image.

## Slide 19: Hough Circle Transform
The Hough Circle Transform extends the idea to detect circles in an image.
For each pixel in the edge-detected image, a circle is parameterized by its center coordinates (x, y) and radius (r).
These parameters form a 3D Hough space, and voting is performed for possible circles.
The peaks in the Hough space represent the centers and radii of the detected circles.

## Slide 20: General Steps of Hough Transform
Edge Detection:
  Compute the edges in the image using appropriate edge detection algorithms (usually Canny).
Hough Accumulator Space:
  Create an accumulator space (Hough space) to represent the parameter space for the shapes being detected.
  Each point in the image contributes to curves or surfaces in this space.
Voting:
  For each edge point in the image, contribute to the corresponding curves or surfaces in the Hough space.
Peak Detection:
  Identify peaks in the Hough space, which correspond to the parameters of the detected shapes.
Thresholding:
  Apply a threshold to the peaks to determine the most significant shapes.

## Slide 21: Hough Transform Algorithm
Extract edges of the image
Initialize parameter space r’s, theta’s
Create accumulator array and initialize to zero
For each edge pixel
  For each theta
    Calculate r = x cos(theta) + y sin(theta)
    Increment accumulator at r, theta
Find Maximum values in accumulator (lines)
Extract related r, theta
rho = distance from the origin to the line along a vector perpendicular to the line
theta = angle in degrees between the x-axis and this vector

## Slide 22: Hough Transform – Merits and Demerits
Merits
Robustness to Noise
Generalization to Arbitrary Shapes
Tolerant to Partial Occlusion
Invariance to Rotation
Useful for Feature Extraction
Applications in Computer Vision
Demerits
Computational Complexity
Accumulator Space Resolution
Sensitivity to Parameter Settings
Limited to Parametric Representations
Limited for Dense or Continuous Shapes
Memory Requirements

## Slide 23: Wavelet Transform
Analyzing and representing images in terms of localized frequency components
Multi-resolution analysis
  Detailed representation of both high and low-frequency components within an image
Wavelets:
  Mathematical functions localized in both time and frequency domains
  Represent signals or images with better time and frequency localization compared to other transforms like Fourier

## Slide 24: Wavelet Transform – key concepts
Image Decomposition and Multiresolution Analysis:
  Wavelet transforms decompose an image into different levels or scales, applying a series of filters successively.
  It reveals details at various resolutions.
  Different scales of details in an image can be captured separately.
Two Components:
  Wavelet transforms typically produce two sets of coefficients, obtained at different decomposition levels :
    Approximation coefficients (representing low-frequency components)
    Detail coefficients (representing high-frequency components).
Image Compression:
  The decomposition into approximation and detail coefficients allows for efficient coding.
  Certain coefficients with lower magnitude can be discarded without significant loss of image quality.
Feature Extraction:
  The coefficients obtained at different scales can capture important structural information, making them valuable for computer vision tasks.
Denoising and Image Enhancement:
  By thresholding or manipulating the detail coefficients, noise can be reduced while preserving and/or enhancing important image features.

## Slide 25: Discrete Wavelet Transform - Algorithm
1D-DWT
2D-DWT

## Slide 26: 2D-DWT – Process
Filtering process
Decomposition

## Slide 27: 2D-DWT – Examples

## Slide 28: Wavelet Transform – Merits and Demerits
Merits
Multiresolution Analysis
Localization in Time and Frequency
Adaptability to Signal Characteristics
Sparse Representation
Energy Compression
Edge Detection and Feature Extraction
Applications in Image Processing
Real-Time Processing
Demerits
Shift Variance
Boundary Effects
Complexity of Implementation
Selection of Wavelet Basis
Limited Directionality
Loss of Phase Information
Trade-Off in Time and Frequency Resolution

## Slide 29: Parametric Transformation
Geometric Transformations:
  Euclidean/Rigid Transform:
    Rotation
    Translation
  Similarity Transform:
    Scaling
    Scaled Rotation
  Affine Transformation
  Perspective/Projective Transform

## Slide 30: Mesh-based Warping
Also known as mesh warping or grid warping
Used to deform or distort an image by manipulating a mesh or grid overlaying the original image.
Goal:
  Achieve non-rigid transformations that can be applied to specific regions of an image while leaving other regions unchanged.
Often employed in computer graphics, image registration, and computer vision applications.
Basic idea:
  Defining a set of control points on a regular grid overlaid onto the image.
  Each control point is associated with a corresponding point in the transformed image.
  By adjusting the positions of these control points, the image is deformed or warped accordingly.
The transformation can be linear or non-linear, allowing for flexible manipulation of the image.

## Slide 31: Key steps in Mesh warping
Grid Initialization:
  Overlay a regular grid on the original image (typically defined by rows and columns of control points).
Control Point Placement:
  Place control points at key locations on the grid
  These points serve as the anchors for the deformation.
  The number and arrangement of control points can vary based on the application.
Define Correspondences:
  Associate each control point in the original grid with a corresponding point in the transformed image.
  This establishes a correspondence/link between the control points of the original and transformed images.
Adjust Control Point Positions:
  Modify the positions of the control points to achieve the desired deformation.
  The movement of control points affects the surrounding pixels, resulting in a non-rigid transformation.
Interpolation:
  Interpolate pixel values between control points to fill in the transformed image.

## Slide 32: Mesh Warping – Example

## Slide 33: Mesh Warping – example